## Slide 1
CAMBRIDGE AS & A LEVEL · PHYSICS 9702 · TOPIC 6
Deformation
of Solids
Hooke's law · stress, strain & Young modulus · strain energy
Syllabus 6.1 – 6.2 | Exams 2025 – 2027
WA
Waseem Ahmad
Head of Science & IB Physics Lead Teacher
Presidential School, Jizzakh · Cambridge Examiner
Author, Orange Publication · www.examspath.com

## Slide 2
SYLLABUS 6.1 – 6.2 · DEFORMATION OF SOLIDS
What the syllabus asks you to do
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
2
1
LO 6.1.1
Deformation is caused by tensile or compressive forces (1D only)
2
LO 6.1.2
Use load, extension, compression and limit of proportionality
3
LO 6.1.3
Recall and use Hooke's law
4
LO 6.1.4
Recall and use k = F / x
5
LO 6.1.5
Define and use stress, strain and the Young modulus
6
LO 6.1.6
Describe an experiment to find the Young modulus of a wire
7
LO 6.2.1
Elastic deformation, plastic deformation and elastic limit
8
LO 6.2.2
Area under a force–extension graph = work done
9
LO 6.2.3
Elastic PE from the area under the graph (within the limit of proportionality)
10
LO 6.2.4
Recall and use E = ½Fx = ½kx²

## Slide 3
TOPIC 6 · DEFORMATION OF SOLIDS
Lesson roadmap
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
3
01
Deformation & Hooke's law
Tension, compression, F = kx
02
Springs in combination
Series and parallel
03
Stress, strain & Young modulus
σ = F/A, ε = x/L, E = σ/ε
04
Measuring E
The wire experiment
05
Elastic & plastic
Limits, brittle, ductile, polymers
06
Strain energy
Area under F–x graph, ½Fx = ½kx²
07
Past paper practice
MCQs and structured questions
08
Doubts & exam tips
Misconceptions and technique

## Slide 4
01
Deformation and Hooke's law
Tensile and compressive forces · F = kx
LEARNING OUTCOMES 6.1.1 – 6.1.4
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
4

## Slide 5
6.1.1 & 6.1.2 · FORCES CHANGE SHAPE AS WELL AS MOTION
Tensile and compressive forces
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
5
Deformation: a change in size or shape caused by forces
Tensile forces stretch → extension
Compressive forces squash → compression
Load: the force applied. Tensile strength: the stress a material can take before it breaks.

## Slide 6
6.1.3 · EXTENSION IS PROPORTIONAL TO LOAD
Hooke's law
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
6
F = kx
k = spring constant (N m⁻¹)
Hooke's law:
the extension of a material is directly proportional to the applied force (load), up to the limit of proportionality. Beyond it the F–x graph curves. The law also applies to compression.

## Slide 7
6.1.4 · K = F / X, A MEASURE OF STIFFNESS
The spring constant
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
7
k = F / x
force per unit extension (N m⁻¹)
Stiffer spring → larger k → smaller extension for the same force
k = gradient of the F–x graph in the straight-line region
Limit of proportionality: the point beyond which F is no longer proportional to x
Worked example
A spring is stretched with increasing load (graph of length against load).
Gradient = Δlength / Δload = 0.045 m / 0.36 N = 0.125 m N⁻¹
k = 1 / gradient = 8.0 N m⁻¹
Careful: this graph has F on the x-axis, so k is 1/gradient.

## Slide 8
02
Springs in combination
Series and parallel arrangements
EXTENSION OF 6.1.3 – 6.1.4
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
8

## Slide 9
COMBINING SPRING CONSTANTS
Springs in series and parallel
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
9
Series (end to end)
Same force in each spring; extensions add. 1/k = 1/k₁ + 1/k₂ — the combination is LESS stiff.
Parallel (side by side)
Same extension; forces add. k = k₁ + k₂ — the combination is STIFFER.
Series: 10 N mm⁻¹ and 5 N mm⁻¹ → 1/k = 1/10 + 1/5 → k = 3.3 N mm⁻¹

## Slide 10
SERIES AND PARALLEL TOGETHER
Worked example · Mixed arrangement
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
10
Springs O, P and Q are identical with spring constant k. Spring R has spring constant 4k. What is the increase in overall length when a force W is applied?
1
O, P and Q in parallel: k(OPQ) = k + k + k = 3k
2
In series with R: 1/k(total) = 1/3k + 1/4k = 7/12k
3
k(total) = 12k / 7
4
x = W / k(total) = 7W / 12k

## Slide 11
03
Stress, strain and the Young modulus
Properties of the material, not the sample
LEARNING OUTCOME 6.1.5
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
11

## Slide 12
6.1.5 · DEFINE AND USE
Stress and strain
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
12
stress σ = F / A
force per unit cross-sectional area · unit Pa (N m⁻²)
strain ε = x / L
extension per unit original length · no unit
Ultimate tensile stress
The maximum force per original cross-sectional area that a wire can support before it breaks.
Why use them?
Extension depends on the size of the sample. Stress and strain remove the effect of A and L, so the results describe the MATERIAL.

## Slide 13
6.1.5 · STIFFNESS OF A MATERIAL
The Young modulus
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
13
E = σ / ε = FL / Ax
unit Pa · the gradient of the linear part of a stress–strain graph
Large E → stiff material (steel ≈ 2 × 10¹¹ Pa)
Small E → easily stretched (rubber ≈ 10⁷ Pa)
Valid only below the limit of proportionality
Strain has no unit, so E has the same unit as stress: pascal (Pa).

## Slide 14
6.1.5 · CALCULATING E
Worked example · Metal wire
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
14
A metal wire hangs from a fixed point and supports a 92 N load. The cross-sectional area is 0.04 mm² and the wire obeys Hooke's law. Its length increases by 0.50%. What is the Young modulus?
1
Convert area: 0.04 mm² = 0.04 × 10⁻⁶ m² = 4 × 10⁻⁸ m²
2
Stress σ = F / A = 92 / 4 × 10⁻⁸ = 2.3 × 10⁹ Pa
3
Strain ε = 0.50% = 0.0050
4
E = σ / ε = 2.3 × 10⁹ / 0.0050 = 4.6 × 10¹¹ Pa
Common traps
mm² → m²: multiply by 10⁻⁶, not 10⁻³
A percentage strain must be divided by 100
Area from diameter: A = πd² / 4

## Slide 15
6.1.5 · GRADIENT OF THE STRAIGHT LINE
Worked example · Reading E from graphs
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
15
Material A
E = 15 × 10⁶ / 0.001 = 1.5 × 10¹⁰ Pa = 15 GPa (strain 0.1% = 0.001)
Material B
E = 12 × 10⁶ / 0.0024 = 5.0 × 10⁹ Pa = 5.0 GPa. A is stiffer; B breaks without plastic flow (brittle).
Convert % strain to a number before dividing.

## Slide 16
04
Measuring the Young modulus
Experiment with a long metal wire
LEARNING OUTCOME 6.1.6
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
16

## Slide 17
6.1.6 · DESCRIBE AN EXPERIMENT
Experiment: Young modulus of a wire
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
17
1
Measure L
original length (≈ 2–3 m) from clamp to marker with a metre rule or tape
2
Measure d
diameter with a micrometer at several points and orientations; A = πd² / 4
3
Add loads
add masses in steps; read the marker's extension x each time with the metre rule (or a vernier)
4
Repeat on unloading
check the wire returns to zero: still elastic

## Slide 18
6.1.6 · FROM GRAPH TO E
Analysis and precautions
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
18
Analysis
Calculate σ = F/A and ε = x/L for each load
Plot σ against ε; E = gradient of the straight line
(or plot F against x: E = gradient × L / A)
Precautions
Long, thin wire → larger, more measurable extension
Straighten kinks with a small initial load first
Wear safety goggles — the wire may snap
A second, unloaded reference wire (Searle's method) cancels thermal expansion and sagging.

## Slide 19
05
Elastic and plastic behaviour
Elastic limit, brittle, ductile and polymeric materials
LEARNING OUTCOME 6.2.1
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
19

## Slide 20
6.2.1 · DOES IT RETURN TO ITS ORIGINAL SHAPE?
Elastic and plastic deformation
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
20
Elastic deformation
When the load is removed, the object returns to its original shape and length.
Plastic deformation
When the load is removed, the object does NOT return to its original shape — a permanent extension remains.
Elastic limit
The point beyond which the object does not return to its original length when the load is removed.
Exam tip
The limit of proportionality (end of Hooke's law) and the elastic limit are close but different. The elastic limit is slightly higher.

## Slide 21
6.2.1 · SHAPES OF STRESS–STRAIN GRAPHS
Brittle, ductile and polymeric materials
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
21
Brittle
straight line to breaking; little or no plastic region — glass, concrete, cast iron
Ductile
straight line, then curves towards the x-axis; large plastic region — copper, steel
Polymeric
non-linear; large strain; rubber stiffens at high strain

## Slide 22
6.2.1 · WHAT THE UNLOADING CURVE TELLS YOU
Loading and unloading
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
22
Rubber: returns to zero (elastic) but by a different path; the area between the curves is energy converted to heat (hysteresis).
Metal past its elastic limit: unloads parallel to the loading line, leaving a permanent extension (plastic).

## Slide 23
06
Elastic potential energy
Work done = area under the force–extension graph
LEARNING OUTCOMES 6.2.2 – 6.2.4
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
23

## Slide 24
6.2.2 & 6.2.3 · WORK DONE IN STRETCHING
Strain energy = area under the F–x graph
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
24
Work done = force × distance moved
So the area under an F–x graph = work done in stretching
Stored as elastic potential (strain) energy if the deformation is elastic
E = ½Fx = ½kx²
within the limit of proportionality (triangle area)
Derivation:
area of triangle = ½ × base × height = ½ × x × F; with F = kx this gives ½kx².

## Slide 25
6.2.3 · AREA OF A TRIANGLE
Worked example · Energy stored in a spring
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
25
A spring is extended with varying forces (graph). What is the energy stored when the extension is 40 mm?
1
Read F at 40 mm: 8.0 N
2
Convert: 40 mm = 0.040 m
3
E = ½ × 0.040 × 8.0
4
E = 0.16 J
Alternatively: k = 200 N m⁻¹ and E = ½kx² = ½ × 200 × 0.040² = 0.16 J

## Slide 26
6.2.2 · SPLIT THE AREA INTO SHAPES
Worked example · Beyond the limit of proportionality
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
26
A metal sample is stretched until it starts to deform plastically. Find the total work done from 0 to 13.5 mm. Treat XY as a straight line.
1
Triangle 0 → X: ½ × 450 × 11.0 × 10⁻³ = 2.48 J
2
Trapezium X → Y: ½ × (450 + 600) × 2.5 × 10⁻³ = 1.31 J
3
Total work = 2.48 + 1.31 = 3.8 J
4
Only the elastic part is recoverable as strain energy

## Slide 27
6.2.3 · AREA OF A TRAPEZIUM
Worked example · Change in strain energy
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
27
The F–x graph for a wire is shown. A gust of wind increases the tension from 140 N to 210 N. Calculate the change in strain energy.
1
From the graph: 140 N at 0.40 mm, 210 N at 0.60 mm
2
ΔE = area of the trapezium
3
ΔE = ½ × (140 + 210) × 0.20 × 10⁻³
4
ΔE = 0.035 J
Or: ½kx₂² − ½kx₁² with k = 3.5 × 10⁵ N m⁻¹ (9702/22 March 2020).

## Slide 28
6.2.4 · RECALL AND USE ½FX AND ½KX²
Quick practice · Elastic potential energy
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
28
Rubber band
A force of 12 N extends a rubber band by 18 cm. Estimate the energy stored.
E ≈ ½ × 12 × 0.18 = 1.1 J — only an estimate, because rubber does not obey Hooke's law.
Stiff spring
A spring with k = 4800 N m⁻¹ is compressed by 2.0 mm. Calculate the energy stored.
E = ½ × 4800 × (0.0020)² = 9.6 × 10⁻³ J

## Slide 29
07
Past paper practice
Paper 1 multiple choice · Paper 2 structured questions
CAMBRIDGE PAST PAPER QUESTIONS
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
29

## Slide 30
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set A · Springs
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
30
1
A mass hangs from two springs in series with stiffness 10 N mm⁻¹ and 5 N mm⁻¹. What is the equivalent stiffness?
A 0.3 N mm⁻¹
B 3.3 N mm⁻¹
C 5 N mm⁻¹
D 15 N mm⁻¹
2
Springs O, P and Q each have spring constant k; R has 4k. What is the increase in overall length when force W is applied?
A 12k / 7W
B 6W / 5k
C 7W / 12k
D 2W / 5
3
A 2.0 N force stretches a spring from 0.50 m to 0.90 m (graph). How much strain energy is stored?
A 1.8 J
B 0.90 J
C 0.40 J
D 0.80 J

## Slide 31
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper · Rubber band
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
31
4
Which graph represents the force–extension relationship of a rubber band stretched almost to its breaking point?
Choose A, B, C or D

## Slide 32
ANSWERS AND KEY WORKING
Answers · Questions 1 – 4
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
32
1
Answer B
Series: 1/k = 1/10 + 1/5 = 3/10 → k = 3.3 N mm⁻¹ (less than either spring).
2
Answer C
Parallel 3k in series with 4k: k(total) = 12k/7, so x = W / k(total) = 7W / 12k.
3
Answer C
Extension = 0.40 m (not 0.90 m). E = ½ × 2.0 × 0.40 = 0.40 J.
4
Answer A
Rubber stiffens as it approaches breaking — the gradient increases sharply at large extension.

## Slide 33
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set B · Stress, strain, Young modulus
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
33
5
To measure the Young modulus of a wire, which measurement is NOT made directly with the listed apparatus?
A extension — vernier scale
B cross-sectional area — micrometer
C original length — metre rule
D mass of load — electronic balance
6
Which is the definition of the ultimate tensile stress of a material?
A max inter-atomic force before bonds break
B max force on a bar before it bends
C max tensile force in a wire before it breaks
D max stretching force per unit cross-sectional area before breaking
7
A glass rod is put under stress until it breaks; its stress–strain graph is a straight line to the end. Which statement is correct?
A the glass shows plastic deformation
B doubling the area halves the UTS
C Hooke's law is obeyed up to breaking
D the glass is ductile
8
A material obeys Hooke's law, has Young modulus E and a tensile stress S. What is the elastic energy stored per unit volume?
A E / 2S²
B S² / E
C S² / 2E
D 2E / S²

## Slide 34
ANSWERS AND KEY WORKING
Answers · Questions 5 – 8
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
34
5
Answer B
The micrometer measures the DIAMETER; area is then calculated with A = πd²/4.
6
Answer D
UTS is a stress: maximum force per (original) cross-sectional area before breaking.
7
Answer C
A straight line through the origin to the breaking point: proportional throughout, brittle, no plastic region.
8
Answer C
Energy per unit volume = ½σε, and ε = σ/E, so ½S × S/E = S²/2E.

## Slide 35
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set C · Graphs and energy
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
35
9
A metal sample is loaded until it fractures. What is the behaviour of the metal between X and Y?
A both elastic and plastic
B not elastic and not plastic
C plastic but not elastic
D elastic but not plastic
10
A metal is stretched from 0 to 12.0 mm (graph). What is the work done? Treat SY as a straight line.
A 6.60 J
B 3.60 J
C 3.55 J
D 3.30 J
11
A force compresses a mattress spring from 100 mm (graph of F against length L). What is the energy stored when L = 70 mm?
A 0.63 J
B 0.27 J
C 0.21 J
D 0.090 J
12
A graph shows the force applied to a rubber cord. What is the maximum strain energy in this deformed cord?
A 200 J
B 5.1 J
C 2.5 J
D 1.9 J

## Slide 36
ANSWERS AND KEY WORKING
Answers · Questions 9 – 12
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
36
9
Answer C
Straight to X (elastic); the curve from X to Y means the elastic limit is passed — plastic deformation until it fractures.
10
Answer C
½ × 500 × 0.010 = 2.50 J plus ½ × (500 + 550) × 0.002 = 1.05 J → 3.55 J.
11
Answer D
k = 12 N / 60 mm; at L = 70 mm, compression 30 mm and F = 6 N: E = ½ × 6 × 0.030 = 0.090 J.
12
Answer D
Count squares: ≈ 0.45 + 0.6 + 0.9 ≈ 1.9 J (remember cm → m). 200 J forgets the conversion.

## Slide 37
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set D · Strain energy and behaviour
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
37
13
The stress–strain graph for a metal is shown. When the strain is 0.010, what is the strain energy per unit volume?
A 10 kJ m⁻³
B 10 MJ m⁻³
C 100 kJ m⁻³
D 1.0 MJ m⁻³
14
A student shades the area under a graph for a metal wire; the area shows the total strain energy. How should the axes be labelled (Y, X)?
A mass, extension
B force, extension
C strain, energy
D stress, strain
15
A sample is loaded to a maximum force then unloaded. On contraction it follows the same curve (S to T) as when stretched. What is its behaviour between S and T?
A both elastic and plastic
B elastic but not plastic
C not elastic and not plastic
D plastic but not elastic

## Slide 38
ANSWERS AND KEY WORKING
Answers · Questions 13 – 15
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
38
13
Answer B
Energy per unit volume = ½σε = ½ × 2 × 10⁹ × 0.010 = 1.0 × 10⁷ J m⁻³ = 10 MJ m⁻³.
14
Answer B
Area under a force–extension graph = work done = strain energy. (Stress–strain area gives energy per unit volume.)
15
Answer B
Returning along the same curve means no permanent change: elastic, even though the graph is curved (not Hooke's law).

## Slide 39
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 1 · Four springs
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
39
The figure shows the force–extension graphs for four springs, A, B, C and D.
(a) State which spring has the greatest value of force constant.
(b) State which spring is the least stiff.
(c) State which of the four springs does not obey Hooke's law.

## Slide 40
MARK SCHEME STYLE SOLUTION
Past paper 1 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
40
(a)
Spring D — the graph has the steepest gradient
(b)
Spring A — it extends the most for each unit of force applied (smallest gradient)
(c)
Spring C — no section of the graph forms a straight line through the origin

## Slide 41
PAPER 2 STYLE · STRUCTURED QUESTION
Worked example · Identify the materials
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
41
Cylindrical samples of steel, glass and rubber are each subjected to a gradually increasing tensile force F. The extensions e are measured and graphs X, Y and Z are plotted.
Correctly label the graphs with the materials: steel, glass, rubber.
Explain your choice for each graph.

## Slide 42
MARK SCHEME STYLE SOLUTION
Worked example · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
42
X = rubber
Non-linear throughout; extends considerably before breaking with little force; stiffens at large extension
Y = steel
Linear (elastic) region, then curves over into a large plastic region — ductile
Z = glass
Straight line up to breaking with no plastic region — brittle

## Slide 43
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 2 · Points on a force–extension graph
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
43
The figure shows the force–extension graph for a wire. The wire is loaded to D and then the load is removed; it returns along the dashed line to E.
(a) Which point shows the limit of proportionality?
(b) Which point shows the elastic limit?
(c) What does the length OE represent?

## Slide 44
MARK SCHEME STYLE SOLUTION
Past paper 2 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
44
(a)
B — the end of the straight-line section
(b)
C — beyond this the wire does not return to its original length
(c)
The permanent (plastic) extension; the unloading line is parallel to the original straight line

## Slide 45
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 3 · Young modulus of steel
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
45
A piece of steel wire, 200.0 cm long and with cross-sectional area 0.50 mm², is stretched by a force of 50 N. Its new length is 200.1 cm.
(a) Calculate the stress in the wire.
(b) Calculate the strain.
(c) Calculate the Young modulus of steel.

## Slide 46
MARK SCHEME STYLE SOLUTION
Past paper 3 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
46
(a)
σ = F / A = 50 / (0.50 × 10⁻⁶) = 1.0 × 10⁸ Pa (0.5 mm² = 0.5 × 10⁻⁶ m²)
(b)
ε = x / L = 0.1 / 200.0 = 5.0 × 10⁻⁴ (0.05%)
(c)
E = σ / ε = 1.0 × 10⁸ / 5.0 × 10⁻⁴ = 2.0 × 10¹¹ Pa

## Slide 47
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 4 · Extension of a copper wire
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
47
Calculate the extension of a copper wire of length 1.00 m and diameter 1.00 mm when a tensile force of 10 N is applied to the end of the wire. The Young modulus of copper is 130 GPa.
(a) Rearrange E = FL / Ax to make x the subject.
(b) Calculate the cross-sectional area.
(c) Calculate the extension.

## Slide 48
MARK SCHEME STYLE SOLUTION
Past paper 4 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
48
(a)
x = FL / AE
(b)
A = πd² / 4 = π × (1.00 × 10⁻³)² / 4 = 7.85 × 10⁻⁷ m²
(c)
x = 10 × 1.00 / (7.85 × 10⁻⁷ × 130 × 10⁹) = 9.8 × 10⁻⁵ m

## Slide 49
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 5 · Glass fibre
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
49
In an experiment to measure the Young modulus of glass, a student draws out a glass rod into a fibre 0.800 m long. Using a travelling microscope she estimates its diameter to be 0.40 mm. The fibre snaps when a 1.00 N load is hung on the end; she judges it extended by no more than 1 mm before it snapped.
(a) Use these values to estimate the Young modulus of the glass.
(b) Explain how the actual or accepted value might differ from this estimate.

## Slide 50
MARK SCHEME STYLE SOLUTION
Past paper 5 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
50
(a)
σ = 4F / πd² = 4 × 1.00 / (π × (0.0004)²) = 8.0 × 10⁶ Pa; ε = 0.001 / 0.800 = 1.25 × 10⁻³ (at most); E ≈ 6.4 × 10⁹ Pa
(b)
The extension may have been LESS than 1 mm, so the strain is smaller and E could be larger. The diameter estimate is also uncertain (d is squared).

## Slide 51
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 6 · Two polymers
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
51
The figure shows force–extension graphs for two polymers, A and B, up to the point where each breaks. For each statement, explain how you deduce your answer from the graphs.
(a) State which polymer has the greater stiffness.
(b) State which polymer requires the greater force to break it.
(c) State which polymer requires the greater amount of work to be done to break it.

## Slide 52
MARK SCHEME STYLE SOLUTION
Past paper 6 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
52
(a)
A — steeper gradient: less extension per unit force
(b)
A — its line continues to a higher force value
(c)
B — larger area under its graph

## Slide 53
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 7 · Pre-stressed railway line
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
53
To allow for expansion in summer, a steel rail laid in cold weather is pre-stressed by a force of 2.6 × 10⁵ N. Its cross-sectional area is 5.0 × 10⁻³ m². A strain of 1.4 × 10⁻⁵ is caused by each °C rise in temperature. The Young modulus of the steel is 2.1 × 10¹¹ Pa.
(a) State and explain whether the force applied when the rail is laid should be tensile or compressive.
(b)(i) Calculate the strain produced when the rail is laid.
(b)(ii) Calculate the temperature rise when the rail becomes unstressed.

## Slide 54
MARK SCHEME STYLE SOLUTION
Past paper 7 · Solution
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
54
(a)
Tensile — the rail expands on heating, which reduces the tensile stress; it becomes unstressed when the temperature is higher
(b)(i)
σ = 2.6 × 10⁵ / 5.0 × 10⁻³ = 5.2 × 10⁷ Pa; ε = σ / E = 5.2 × 10⁷ / 2.1 × 10¹¹ = 2.5 × 10⁻⁴
(b)(ii)
Temperature rise = 2.48 × 10⁻⁴ / 1.4 × 10⁻⁵ = 17.7 ≈ 18 °C

## Slide 55
COMMON DOUBTS & MISCONCEPTIONS
Students often ask… (1)
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
55
?
“Is the limit of proportionality the same as the elastic limit?”
No. The LoP is where F stops being proportional to x; the elastic limit is where permanent deformation starts. They are close but different.
?
“Does a curved F–x graph mean plastic deformation?”
Not necessarily. Rubber has a curved graph but still returns to its original length — it is elastic, just not Hookean.
?
“Does a thicker wire have a larger Young modulus?”
No. E is a property of the material. A thicker wire has a larger spring constant k, but the same E.
?
“Why does my Young modulus come out 10³ times too big?”
Usually mm² was converted with 10⁻³ instead of 10⁻⁶, or a percentage strain was not divided by 100.

## Slide 56
COMMON DOUBTS & MISCONCEPTIONS
Students often ask… (2)
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
56
?
“Can I always use E = ½kx²?”
Only within the limit of proportionality. Otherwise use the area under the F–x graph.
?
“Are two springs in series stiffer?”
No — less stiff. The same force acts on each, so the extensions add. Springs in parallel are stiffer.
?
“Is all the work done stored as strain energy?”
Only for elastic deformation. In plastic deformation (and rubber hysteresis) some energy becomes internal (thermal) energy.
?
“Is a brittle material weak?”
Not necessarily. Glass and diamond can have high tensile strength; brittle means little or no plastic deformation before breaking.

## Slide 57
COMMAND WORDS AND MARK-SCHEME HABITS
Exam technique for deformation of solids
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
57
Define
stress: force per unit cross-sectional area; strain: extension per unit original length; E = stress / strain
Units
convert mm → m and mm² → m² (× 10⁻⁶); strain has no unit; E in Pa
Hooke's law
‘extension is proportional to force, up to the limit of proportionality’
Energy
½Fx only for straight-line graphs; otherwise count squares or split into shapes
Describe the experiment
long thin wire, micrometer for d, rule for L, marker for x, plot σ against ε
Materials
brittle = straight to breaking; ductile = large plastic region; polymer = curved

## Slide 58
KEY IDEAS TO TAKE AWAY
Deformation in one slide
F = kx
σ = F / A
ε = x / L
E = FL / Ax
Limits
limit of proportionality → elastic limit → plastic → UTS → breaking
Energy
area under F–x = work done · E = ½Fx = ½kx² within the limit of proportionality
Springs
series: 1/k = 1/k₁ + 1/k₂ · parallel: k = k₁ + k₂
Topic 6 · Deformation of solids | Cambridge International AS Level Physics 9702
58