## Slide 1
CAMBRIDGE AS & A LEVEL · PHYSICS 9702 · TOPICS 9 & 10
Electricity
& D.C. Circuits
Current · power · resistivity · e.m.f. · Kirchhoff · dividers
Syllabus 9.1 – 10.3 | Exams 2025 – 2027
WA
Waseem Ahmad
Head of Science & IB Physics Lead Teacher
Presidential School, Jizzakh · Cambridge Examiner
Author, Orange Publication · www.examspath.com

## Slide 2
SYLLABUS 9.1 – 10.3 · ELECTRICITY AND D.C. CIRCUITS
What the syllabus asks you to do
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
2
9.1 Electric current
current is a flow of charge carriers · charge is quantised · Q = It · I = Anvq
9.2 P.d. and power
p.d. = energy per unit charge · V = W/Q · P = VI = I²R = V²/R
9.3 Resistance & resistivity
R = V/I · I–V graphs (metal, diode, lamp) · Ohm's law · R = ρL/A · LDR and thermistor
10.1 Practical circuits
circuit symbols · e.m.f. vs p.d. · internal resistance and terminal p.d.
10.2 Kirchhoff's laws
first law (charge) · second law (energy) · derive series and parallel formulae · solve circuits
10.3 Potential dividers
principle · potentiometer comparing p.d.s · galvanometer null methods · thermistor and LDR sensors

## Slide 3
TOPICS 9 & 10 · ELECTRICITY AND D.C. CIRCUITS
Lesson roadmap
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
3
01
Current & charge
Q = It, I = Anvq
02
P.d. & power
V = W/Q, P = VI
03
Resistance & I–V
Ohm's law, lamp, diode
04
Resistivity & sensors
R = ρL/A, LDR, thermistor
05
E.m.f. & internal r
E = I(R + r)
06
Kirchhoff's laws
Junctions and loops
07
Potential dividers
Sensors, potentiometer
08
Practice & doubts
Past papers, misconceptions

## Slide 4
01
Electric current and charge
Current is a flow of charge carriers
LEARNING OUTCOMES 9.1.1 – 9.1.4
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
4

## Slide 5
9.1.1 & 9.1.3 · RATE OF FLOW OF CHARGE
Electric current
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
5
Q = It
charge (C) = current (A) × time (s); 1 C = 1 A s
Current: the rate of flow of charge carriers
In metals the carriers are free electrons; in electrolytes, ions
Conventional current flows from + to −, opposite to electron flow
Ammeter: connected in series; ideally zero resistance
Quick check:
0.40 A for 15 s → Q = 6.0 C; 150 C in 30 s → I = 5.0 A; 50 C in 20 s → I = 2.5 A

## Slide 6
9.1.2 · Q = NE
Charge is quantised
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
6
Q = ne
n = whole number; e = 1.60 × 10⁻¹⁹ C
Charge comes in whole-number multiples of the elementary charge e. A proton carries +e and an electron −e — no smaller free charge exists.
Protons in 1 C
n = 1 / 1.60 × 10⁻¹⁹ = 6.3 × 10¹⁸
Which is possible?
6.0 × 10⁻¹⁹ C = 3.75e ✗; 8.0 × 10⁻¹⁹ C = 5e ✓; 10.0 × 10⁻¹⁹ C = 6.25e ✗ — only exact multiples of e
Car battery 50 A h
at 200 A lasts ¼ h = 15 min; charge = 200 × 900 = 1.8 × 10⁵ C

## Slide 7
9.1.4 · NUMBER DENSITY AND DRIFT SPEED
Current in a conductor: I = Anvq
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
7
n: number density (carriers per m³)
A: cross-sectional area (m²)
v: mean drift speed (m s⁻¹)
q: charge of each carrier (C)
Worked example:
a copper wire (n = 8.2 × 10²⁸ m⁻³, A = 1.5 mm²) carries 3.5 A. v = I / nAq = 3.5 / (8.2 × 10²⁸ × 1.5 × 10⁻⁶ × 1.60 × 10⁻¹⁹) = 1.8 × 10⁻⁴ m s⁻¹ — only about 0.18 mm per second! The current is set up almost instantly because n is enormous.

## Slide 8
9.1.4 · USING I = ANVQ
Worked examples · Drift speed
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
8
Gold wire
A = 2.0 mm², v = 0.10 mm s⁻¹, n = 5.9 × 10²⁸ m⁻³
I = 5.9 × 10²⁸ × 2.0 × 10⁻⁶ × 1.0 × 10⁻⁴ × 1.6 × 10⁻¹⁹ = 1.9 A
Copper wire
diameter 1.0 mm, I = 5.0 A, n = 8.5 × 10²⁸ m⁻³
v = 5.0 / (8.5 × 10²⁸ × π(0.50 × 10⁻³)² × 1.6 × 10⁻¹⁹) = 4.7 × 10⁻⁴ m s⁻¹
Copper → silver
same current and size; silver n = 5.9 × 10²⁸ m⁻³
v ∝ 1/n, so the drift speed increases in silver (fewer carriers must move faster)
Thin vs thick
same current in wires of different area
v ∝ 1/A: the electrons drift faster in the thinner wire

## Slide 9
02
Potential difference and power
Energy transferred per unit charge
LEARNING OUTCOMES 9.2.1 – 9.2.3
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
9

## Slide 10
9.2.1 & 9.2.2 · V = W / Q
Potential difference
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
10
V = W / Q
1 V = 1 J C⁻¹
Definition:
the potential difference across a component is the energy transferred (from electrical to other forms) per unit charge passing through it. A voltmeter is connected in parallel and ideally has infinite resistance.
Which lamp is brighter?
A 240 V mains lamp and a 12 V car lamp carry the same current. Each coulomb transfers 240 J in the mains lamp but only 12 J in the car lamp — 20 times more energy per second, so the 240 V lamp is far brighter.
Worked example
A lamp carries 10 A for 20 s and transfers 400 J. Charge = 10 × 20 = 200 C; energy per coulomb = 400 / 200 = 2.0 J; so the p.d. = 2.0 V.

## Slide 11
9.2.3 · P = VI = I²R = V²/R
Electrical power
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
11
P = VI
power = rate of transfer of energy
P = I²R
using V = IR
P = V² / R
using I = V/R
Calculator
3.0 V across 20 kΩ: P = V²/R = 9 / 20 000 = 0.45 mW
230 V, 15 W bulb
I = P/V = 0.065 A; R = V/I = 3500 Ω
100 W bulb, 0.43 A
R = P/I² = 100 / 0.43² = 540 Ω
Power station
25 kV, 40 kA: P = VI = 1.0 × 10⁹ W (1 GW)

## Slide 12
9.2 · ENERGY, CHARGE AND POWER
Worked example · Car battery
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
12
A battery has negligible internal resistance, an e.m.f. of 12.0 V and a capacity of 100 A h (ampere-hours). Calculate (i) the total charge it can supply (ii) the total energy it can transfer. It is connected to a 27 W lamp — calculate the lamp's resistance.
Charge
Q = It = 100 A × 3600 s = 3.6 × 10⁵ C
Energy
W = QV = 3.6 × 10⁵ × 12 = 4.3 × 10⁶ J
Resistance
R = V² / P = 12² / 27 = 5.3 Ω
Also:
a 12 V battery supplying 10 A for 5.0 hours transfers W = IVt = 10 × 12 × 18 000 = 2.2 MJ. E.m.f. is the work done per coulomb in the whole circuit; terminal p.d. is the work done per coulomb in the external circuit.

## Slide 13
03
Resistance and I–V characteristics
R = V / I and Ohm's law
LEARNING OUTCOMES 9.3.1 – 9.3.5
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
13

## Slide 14
9.3.1, 9.3.2 & 9.3.5 · DEFINE AND STATE
Resistance and Ohm's law
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
14
R = V / I
1 Ω = 1 V A⁻¹
Resistance:
the ratio of the p.d. across a component to the current through it.
Ohm's law:
for a metallic conductor at constant temperature, the current is directly proportional to the p.d.
Worked example
5.0 C passes through a resistor in 30 s with 2.0 V across it. I = Q/t = 5.0/30 = 0.17 A; R = V/I = 2.0 / 0.167 = 12 Ω
Measuring R
Ammeter in series, voltmeter in parallel
Use a low supply p.d. (1–2 V) so the component does not heat up
Vary with a variable resistor; plot I against V

## Slide 15
9.3.3 · SKETCH AND EXPLAIN THE SHAPES
I–V characteristics
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
15
Metallic conductor
straight line through the origin: constant R (obeys Ohm's law)
Filament lamp
gradient decreases: R increases as I increases because the filament gets hotter
Semiconductor diode
conducts only in forward bias above ≈ 0.6 V; almost zero current in reverse

## Slide 16
9.3.4 · RESISTANCE AND TEMPERATURE
Why a filament's resistance rises
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
16
Explanation chain
1
Larger current → more energy dissipated → filament temperature rises
2
Lattice ions vibrate with larger amplitude
3
Free electrons collide with the ions more often
4
Mean drift speed falls for a given p.d. → resistance increases
Reading the graph
R = V/I at a point (NOT 1/gradient of the tangent). On an I–V graph a decreasing gradient means increasing resistance.
Semiconductors are different
heating releases many more charge carriers, so the number density n rises and resistance FALLS (thermistor).

## Slide 17
04
Resistivity, LDRs and thermistors
R = ρL / A
LEARNING OUTCOMES 9.3.6 – 9.3.8
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
17

## Slide 18
9.3.6 · R = ΡL / A
Resistivity
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
18
R = ρL / A
ρ = resistivity (Ω m): a property of the material
Double the length → double the resistance
Double the diameter → area × 4 → resistance ÷ 4
Resistivity depends on the material and its temperature
copper
1.7 × 10⁻⁸ Ω m
aluminium
2.8 × 10⁻⁸ Ω m
silicon
2.3 × 10³ Ω m
glass
10¹² Ω m
Stretched wire:
a 10 Ω wire stretched to twice its length (same volume) has half the area, so R = 10 × 2 × 2 = 40 Ω.

## Slide 19
9.3.6 · RECALL AND USE R = ΡL/A
Worked examples · Resistivity
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
19
Cylinders
Cu: d = 5 mm, L = 8 mm; Al: d = 10 mm, L = 16 mm
R(Cu) = 1.7 × 10⁻⁸ × 0.008 / π(0.0025)² = 6.9 μΩ; R(Al) = 5.7 μΩ → aluminium conducts better here
1.0 cm³ of copper
drawn into a wire of area 4.0 × 10⁻⁷ m²
L = V/A = 2.5 m; R = ρL/A = 1.69 × 10⁻⁸ × 2.5 / 4.0 × 10⁻⁷ = 0.11 Ω
Same wire, 5 m
a 1.0 m length has R = 0.50 Ω
R ∝ L → 5.0 m has 2.5 Ω; halving the diameter instead → R × 4 = 2.0 Ω
Heater element
ρ = 1.30 × 10⁻⁸ Ω m, A = 0.0080 mm²
1.5 m has R = 1.30 × 10⁻⁸ × 1.5 / 8.0 × 10⁻⁹ = 2.4 Ω; for 30 Ω, L = RA/ρ = 18 m

## Slide 20
9.3.7 & 9.3.8 · SENSORS
LDRs and thermistors
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
20
LDR:
resistance decreases as light intensity increases — used in automatic street lights and light meters.
Thermistor (NTC):
resistance decreases as temperature increases — used in thermostats, fire alarms and thermometers.

## Slide 21
05
E.m.f. and internal resistance
Practical circuits
LEARNING OUTCOMES 10.1.1 – 10.1.5
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
21

## Slide 22
10.1.1 & 10.1.2 · RECALL, DRAW AND INTERPRET
Circuit symbols
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
22
Ammeters go in series (ideal: zero resistance); voltmeters go in parallel (ideal: infinite resistance). A diode's arrow shows the direction of conventional current when it conducts.

## Slide 23
10.1.3 & 10.1.4 · TWO KINDS OF ENERGY TRANSFER
E.m.f. and potential difference
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
23
E.m.f. E
The energy transferred per unit charge from other forms (e.g. chemical) to ELECTRICAL energy in driving charge around a complete circuit.
P.d. V
The energy transferred per unit charge from ELECTRICAL energy to other forms (heat, light) in a component.
Measuring e.m.f.:
connect a high-resistance voltmeter across the cell with no other current flowing (open circuit). Example: a voltmeter reads 3.0 V; when a 10 Ω resistor is connected it drops to 2.8 V → I = 0.28 A, lost volts 0.2 V, r = 0.2 / 0.28 = 0.71 Ω.

## Slide 24
10.1.5 · TERMINAL P.D. AND LOST VOLTS
Internal resistance
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
24
E = I(R + r) = V + Ir
Terminal p.d. V = IR (available to the circuit)
Lost volts = Ir (energy dissipated inside the cell, which warms up)
Worked example
E = 7.3 V, r = 0.30 Ω, R = 9.5 Ω. I = 7.3 / 9.8 = 0.74 A; lost volts = 0.74 × 0.30 = 0.22 V; terminal p.d. = 7.1 V
Larger current → more lost volts → lower terminal p.d.

## Slide 25
10.1.5 · INTERNAL RESISTANCE PROBLEMS
Worked examples · E = I(R + r)
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
25
Single resistor
E = 5.0 V, r = 2.0 Ω, R = 8.0 Ω
I = 5.0 / 10 = 0.50 A
Two 10 Ω in series
E = 3.0 V, r = 4.0 Ω
I = 3.0 / 24 = 0.125 A; lost volts 0.50 V; terminal p.d. 2.5 V
Two 10 Ω in parallel
E = 3.0 V, r = 4.0 Ω; R = 5.0 Ω
I = 3.0 / 9.0 = 0.33 A; lost volts 1.33 V; terminal p.d. 1.67 V
Four cells in series
each 1.5 V, 0.10 Ω; lamp 2.0 Ω
I = 6.0 / (2.0 + 0.40) = 2.5 A

## Slide 26
10.1.5 · V = −RI + E
Finding E and r from a graph
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
26
Method
Connect a variable resistor across the cell; measure V and I for several settings
Plot V (y-axis) against I
Compare with y = mx + c
Results from the table
y-intercept = E ≈ 1.5 V
gradient = −r → r ≈ 0.5 Ω

## Slide 27
06
Kirchhoff's laws
Conservation of charge and energy
LEARNING OUTCOMES 10.2.1 – 10.2.7
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
27

## Slide 28
10.2.1 · CONSEQUENCE OF CONSERVATION OF CHARGE
Kirchhoff's first law
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
28
The sum of the currents entering a junction equals the sum of the currents leaving it.
Example
In: 3 A + 2 A = 5 A. Out: 1 A + 2.5 A + I₅
→ I₅ = 1.5 A (out of the junction)
Charge cannot be created or destroyed at a junction, so the rate of flow in must equal the rate of flow out. In a series circuit the current is the same everywhere.

## Slide 29
10.2.2 · CONSEQUENCE OF CONSERVATION OF ENERGY
Kirchhoff's second law
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
29
Around any closed loop, the sum of the e.m.f.s equals the sum of the p.d.s.
Sign rules
Choose a direction round the loop
e.m.f. positive if it pushes current that way
IR positive if the current flows that way through the resistor
A negative answer means the current flows the opposite way
Worked example
A 10 V battery (negligible r) drives 0.1 A through 20 Ω and R in series. p.d. across 20 Ω = 0.1 × 20 = 2.0 V; so p.d. across R = 10 − 2.0 = 8.0 V; R = 8.0 / 0.1 = 80 Ω

## Slide 30
10.2.3 – 10.2.6 · USING KIRCHHOFF'S LAWS
Deriving series and parallel formulae
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
30
Series
Same current I (first law). Second law: V = V₁ + V₂ + V₃ → IR = IR₁ + IR₂ + IR₃ → R = R₁ + R₂ + R₃
Parallel
Same p.d. V (second law). First law: I = I₁ + I₂ + I₃ → V/R = V/R₁ + V/R₂ + V/R₃ → 1/R = 1/R₁ + 1/R₂ + 1/R₃

## Slide 31
10.2.7 · SOLVE WITH BOTH LAWS
Worked example · Two e.m.f.s
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
31
Find the currents I₁, I₂ and I₃ in the circuit (both cells have negligible internal resistance).
1
First law at P: I₁ + I₂ = I₃
2
Upper loop (6.0 V, 10 Ω, 30 Ω): 6.0 = 10I₁ + 30I₃
3
Lower loop (2.0 V, 30 Ω): 2.0 = 30I₃ → I₃ = 0.067 A
4
Then 10I₁ = 6.0 − 2.0 → I₁ = 0.40 A; I₂ = 0.067 − 0.40 = −0.33 A (it flows the other way)

## Slide 32
07
Potential dividers
Sharing the supply p.d. between resistors
LEARNING OUTCOMES 10.3.1 – 10.3.4
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
32

## Slide 33
10.3.1 · PRINCIPLE
The potential divider
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
33
The p.d. is shared in proportion to the resistances
V₁ / V₂ = R₁ / R₂ (same current)
Vary R₁ or R₂ (or use a sliding contact) to get any output from 0 to the supply p.d.
Worked example
Vout = 5.3 V across 20 kΩ (with 12 kΩ).
Vin = 5.3 × (20 + 12) / 20 = 8.5 V

## Slide 34
10.3.4 · THERMISTORS AND LDRS IN POTENTIAL DIVIDERS
Sensing circuits
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
34
Temperature rises → thermistor R falls → its share of p.d. falls
Light increases → LDR R falls → its share of p.d. falls
Vout across the fixed R rises in both cases
Design tip:
swap the sensor and the fixed resistor to reverse the behaviour — e.g. put the LDR at the top so Vout across the fixed resistor RISES as it gets DARK to switch on a street light.

## Slide 35
10.3.2 & 10.3.3 · COMPARING POTENTIAL DIFFERENCES
The potentiometer and null methods
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
35
A uniform wire XY carries a steady current from the driver cell, so p.d. ∝ length
Move the jockey until the galvanometer reads zero: the null (balance) point
At balance no current flows through the test cell, so its terminal p.d. = its e.m.f.
Comparing cells: E₁ / E₂ = l₁ / l₂
A galvanometer is a sensitive meter used to detect a zero current (null reading).

## Slide 36
08
Past paper practice
Paper 1 multiple choice · Paper 2 structured questions
CAMBRIDGE PAST PAPER QUESTIONS
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
36

## Slide 37
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set A · Current and units
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
37
1
When will 8 mA of current pass through an electrical circuit?
A when 1 J of energy is used by 1 C of charge
B when a charge of 4 C passes in 500 s
C when a charge of 8 C passes in 100 s
D when a charge of 1 C passes in 8 s
2
What is the unit of resistance when expressed in SI base units?
A kg m² s⁻² A⁻¹
B kg m² s⁻³ A⁻²
C kg m s⁻² A⁻¹
D kg m² s⁻³ A⁻¹
3
The unit of resistivity in SI base units is kg x³ y⁻³ z⁻². Which base units are x, y and z?
A ampere, metre, second
B metre, ampere, second
C metre, second, ampere
D second, ampere, metre

## Slide 38
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper · Filament lamp
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
38
4
Which graph shows the I–V characteristic of a filament lamp?
Choose A, B, C or D

## Slide 39
ANSWERS AND KEY WORKING
Answers · Questions 1 – 4
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
39
1
Answer B
I = Q/t = 4 / 500 = 8 × 10⁻³ A = 8 mA. C gives 80 mA; D gives 125 mA; A is a p.d., not a current.
2
Answer B
R = V/I; V = kg m² s⁻³ A⁻¹, so R = kg m² s⁻³ A⁻². (D is the volt.)
3
Answer C
ρ = RA/L → kg m² s⁻³ A⁻² × m² ÷ m = kg m³ s⁻³ A⁻², so x = metre, y = second, z = ampere.
4
Answer D
Current rises steeply at first, then the gradient falls as the filament heats up and its resistance increases.

## Slide 40
PAPER 1 STYLE · MULTIPLE CHOICE
Past paper set B · Circuits
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
40
5
The combined resistance of the series circuit is 60 Ω. What is the resistance of R₂?
A 100 Ω
B 30 Ω
C 20 Ω
D 40 Ω
6
Three resistors R, 2R and R are connected in parallel. What is their combined resistance?
A 5R / 2
B 2 / 5R
C 5 / 2R
D 2R / 5
7
Two lamps are connected in series to a 150 V supply: one is rated 135 V, 41 W and the other 15 V, 4.5 W. What happens?
A both lamps light normally
B the 15 V lamp blows
C only the 41 W lamp lights
D both light at less than normal brightness
8
The resistance of R₁ changes with temperature; the resistance of R₂ changes with illumination. What are these devices?
A thermistor, light-dependent resistor
B thermistor, potential divider
C diode, light-dependent resistor
D diode, potential divider

## Slide 41
ANSWERS AND KEY WORKING
Answers · Questions 5 – 8
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
41
5
Answer C
Series: 60 = 30 + R₂ + 10 → R₂ = 20 Ω.
6
Answer D
1/R_T = 1/R + 1/2R + 1/R = 5/2R → R_T = 2R/5.
7
Answer A
Normal currents: 41/135 = 0.30 A and 4.5/15 = 0.30 A — equal, and 135 + 15 = 150 V, so both work normally in series.
8
Answer A
Temperature → thermistor; illumination → LDR. A potential divider is a circuit, not a device.

## Slide 42
PAPER 1 STYLE · MULTIPLE CHOICE
Set C · Sensors and internal resistance
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
42
9
A thermistor is in series with a resistor R and a battery. At room temperature their resistances are equal. The temperature of the thermistor DECREASES. Which is correct?
A the p.d. across the thermistor increases
B the current in R increases
C the current through the thermistor decreases
D the p.d. across R increases
10
An LDR is in series with a resistor R. With no light the LDR's resistance equals R. Light now falls on the LDR. Which is correct?
A the current in R decreases
B the current through the LDR decreases
C the p.d. across R decreases
D the p.d. across the LDR decreases
11
A potential divider consists of a fixed resistor R above a thermistor. The temperature increases. What happens to the p.d.s across the thermistor and across R?
A thermistor increases, R increases
B thermistor decreases, R increases
C thermistor decreases, R decreases
D thermistor increases, R decreases
12
A car battery of e.m.f. 12 V delivers 100 A to the starter motor; the terminal p.d. falls to 9.0 V. What is the internal resistance?
A 0.03 Ω
B 0.09 Ω
C 0.12 Ω
D 3.0 Ω

## Slide 43
ANSWERS AND KEY WORKING
Answers · Questions 9 – 12
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
43
9
Answer A
Colder → thermistor R rises → it takes a larger share of the p.d. (total current falls; R's p.d. falls).
10
Answer D
Light → LDR resistance falls → current rises → p.d. across R rises, so p.d. across the LDR falls.
11
Answer B
Hotter → thermistor R falls → its p.d. falls and the fixed resistor's p.d. rises.
12
Answer A
Lost volts = 12 − 9.0 = 3.0 V = Ir → r = 3.0 / 100 = 0.03 Ω.

## Slide 44
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 1 · Drift speed (9702/23 M/J 2020)
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
44
The current I in a metal wire is given by I = Anve, where v is the average drift speed of the free electrons and e is the elementary charge. Two lamps P and Q are connected in series. The radius of the filament wire of P is twice that of Q; the filaments are made of metals with the same value of n.
(a) State what is meant by the symbols A and n. [2]
(b) Use the expression to determine the SI base units of e. [2]
(c) Calculate the ratio: average drift speed in P / average drift speed in Q. [2]

## Slide 45
MARK SCHEME STYLE SOLUTION
Past paper 1 · Solution
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
45
(a)
A: cross-sectional area (of the wire); n: number density of free electrons (number per unit volume)
(b)
e = I / Anv → A ÷ (m² × m⁻³ × m s⁻¹) = A s
(c)
Same current in series; v ∝ 1/A = 1/r²; radius of P = 2 × radius of Q → ratio = 1/4 = 0.25

## Slide 46
PAPER 2 STYLE · STRUCTURED QUESTION
Past paper 2 · Battery, X and wire Y (9702/22)
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
46
A battery of e.m.f. 8.0 V and internal resistance 2.0 Ω is connected to resistor X (15 Ω) in parallel with a wire Y. The current in the battery is 2.5 A.
(a) State Kirchhoff's first law and the quantity it conserves. [2]
(b)(i) Calculate the thermal energy dissipated in the battery in 5.0 minutes. [2]
(b)(ii) Calculate the terminal p.d. of the battery and the resistance of Y. [4]
(c) A new wire Z of the same length has less resistance than Y. State two possible differences and the effect on the total power produced by the battery. [3]

## Slide 47
MARK SCHEME STYLE SOLUTION
Past paper 2 · Solution
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
47
(a)
The sum of currents into a junction = sum of currents out of it; charge is conserved
(b)(i)
E = I²rt = 2.5² × 2.0 × 300 = 3750 J (3.8 kJ)
(b)(ii)
V = 8.0 − 2.5 × 2.0 = 3.0 V; I(X) = 3.0 / 15 = 0.20 A; I(Y) = 2.3 A; R(Y) = 3.0 / 2.3 = 1.3 Ω
(c)
Z has a larger diameter (area) or a material of smaller resistivity; total resistance falls, current rises, so the power produced (P = EI) increases

## Slide 48
PAPER 2 STYLE · STRUCTURED QUESTION
Book question · Potential divider
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
48
This circuit shows a potential divider. The battery has negligible internal resistance (9.0 V) and the voltmeter has infinite resistance. R₁ is a variable resistor and R₂ = 470 Ω.
(a) State and explain how the voltmeter reading changes when the resistance of R₁ is increased. [2]
(b) Calculate R₁ when the voltmeter reads 2.0 V. [2]
(c) The voltmeter is replaced with one of resistance 2 kΩ. Calculate its new reading. [3]

## Slide 49
MARK SCHEME STYLE SOLUTION
Book question · Solution
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
49
(a)
The reading decreases: R₁ takes a larger share of the 9.0 V (the current falls, so the p.d. across R₂ falls)
(b)
2.0 / 9.0 = 470 / (470 + R₁) → R₁ = 1645 Ω ≈ 1.6 kΩ
(c)
R₂ ∥ 2 kΩ = 381 Ω; V = 9.0 × 381 / (381 + 1645) = 1.7 V (the voltmeter draws current and lowers the reading)

## Slide 50
PAPER 2 STYLE · STRUCTURED QUESTION
Book question · Internal resistance
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
50
A high-resistance voltmeter placed across an isolated battery reads 3.0 V. When a 10 Ω resistor is connected across the battery, the voltmeter reading drops to 2.8 V.
(a) State the e.m.f. of the battery.
(b) Calculate the current in the circuit.
(c) Determine the internal resistance of the battery.

## Slide 51
MARK SCHEME STYLE SOLUTION
Book question · Solution
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
51
(a)
E = 3.0 V (open-circuit reading of a high-resistance voltmeter)
(b)
I = V / R = 2.8 / 10 = 0.28 A
(c)
lost volts = 3.0 − 2.8 = 0.2 V; r = 0.2 / 0.28 = 0.71 Ω

## Slide 52
PAPER 2 STYLE · STRUCTURED QUESTION
Book question · Thermometers
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
52
The resistance of a metal wire changes with temperature, so a wire could be used to sense changes in temperature, in the same way that a thermistor is used.
(a) Suggest one advantage a thermistor has over a metal wire for this purpose.
(b) Suggest one advantage a metal wire has over a thermistor.
(c) Explain why the resistance of a metal increases with temperature while that of a semiconductor decreases.

## Slide 53
MARK SCHEME STYLE SOLUTION
Book question · Solution
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
53
(a)
A thermistor's resistance changes much more per degree, so it is more sensitive
(b)
A metal wire works over a much wider temperature range, and its resistance changes almost linearly (easier calibration)
(c)
Metal: ions vibrate more, more collisions, lower drift speed. Semiconductor: more electrons gain enough energy to become free, so n increases greatly

## Slide 54
COMMON DOUBTS & MISCONCEPTIONS
Students often ask… (1)
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
54
?
“Is current used up in a lamp?”
No. Charge is conserved: the same current flows in and out. It is ENERGY that is transferred to heat and light.
?
“Is e.m.f. a force?”
No. E.m.f. is energy transferred per unit charge (in volts), despite its name.
?
“Does a filament lamp obey Ohm's law?”
No. Its temperature rises with current, so its resistance increases and the I–V graph curves.
?
“Is resistance the gradient of an I–V graph?”
No. R = V/I at that point. Only for a straight line through the origin does this equal 1/gradient.

## Slide 55
COMMON DOUBTS & MISCONCEPTIONS
Students often ask… (2)
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
55
?
“Why does the terminal p.d. drop when I draw more current?”
Lost volts Ir increase with I, so V = E − Ir decreases.
?
“Does a thicker wire have higher resistivity?”
No. Resistivity is a property of the material. A thicker wire has LOWER resistance, same resistivity.
?
“In a potential divider, why does my voltmeter read low?”
A voltmeter with finite resistance in parallel lowers the combined resistance of that part, reducing its share of the p.d.
?
“Does the galvanometer measure the e.m.f. at balance?”
It shows zero current; at the null point the p.d. along the wire equals the cell's e.m.f.

## Slide 56
COMMAND WORDS AND MARK-SCHEME HABITS
Exam technique for electricity
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
56
Definitions
p.d.: energy per unit charge (electrical → other forms); e.m.f.: other forms → electrical
Units
convert mm² → m² (× 10⁻⁶); A h × 3600 = coulombs; kW h is energy
Kirchhoff
state conservation of charge (1st law) and energy (2nd law); mark current directions
Graphs
R = V/I at a point; V–I graph for a cell: intercept E, gradient −r
Sensors
explain step by step: T ↑ → R(thermistor) ↓ → share of p.d. ↓ → Vout …
Filament lamp
temperature ↑ → lattice vibrations ↑ → more collisions → R ↑

## Slide 57
KEY IDEAS TO TAKE AWAY
Electricity in one slide
Q = It, I = Anvq
P = VI = I²R
R = ρL / A
E = I(R + r)
I–V
metal: straight line · lamp: gradient falls (R rises) · diode: conducts forward only
Kirchhoff
1st: Σ I in = Σ I out (charge) · 2nd: Σ e.m.f. = Σ IR round a loop (energy)
Dividers
Vout = R₂ / (R₁ + R₂) × Vin · thermistor and LDR sensors · potentiometer null method
Topics 9 & 10 · Electricity and D.C. circuits | Cambridge International AS Level Physics 9702
57